## Tesoro – 2007-11 Lagoon 420 – Owner’s Version Catamaran

CONSTRUCTION

• Polyester and vinylester FRP construction (osmotic barrier)

• Balsa core composite hulls - white gel coat infused

• Solid glass FRP under waterline infused

• Balsa core composite deck and bridge deck

• Solid or felt core composite interior FRP hull & roof liners

• FRP reinforced marine ply bulkheads; tabbed or glued to hull

SAILS

• 1 Full batten large roach mainsail, 66,4 m2/ 714 sq ft

• 1 Furling genoa with UV protective band, 35,9 m2 / 386 sq ft

STANDING RIGGING

• Anodized aluminum deck-stepped mast (18 m / 59'1'')

• Single spreaders

• 1 Anodized aluminum boom

• 2 Shroud deck chainplates

• 1 Forestay chainplate on composite central rostrum

RUNNING RIGGING

• 1 Double purchase main halyard

• 1 Genoa halyard

• 1 Double purchase mainsheet led to helm station, mainsheet traveler & car on hard top bimini

• 2 Genoa sheets

• 2 Genoa sheet tracks

• 3 Winches at helm station:

• 1 Winch 46.2ST for:

- Port mainsheet traveler line

- Starboard mainsheet traveler line

- Port Genoa sheet

• 1 Electric Winch 44.2STE for:

- Main halyard

- Genoa halyard

- Optional Spinnaker halyard

- Boom topping lift

• 1 Winch 46.2ST for

- Main sheet

- Reef 1 (automatic)

- Reef 2 (automatic)

- Reef 3 (conventional)

- Starboard genoa sheet

- Genoa furling line

• 3 reefing lines (2 auto and 1 conventional)

• Line jammers

• 1 Fixed Mainsail clew pad-eye

• 1 Genoa furler line

• 2 Adjustable lazy jacks

• 2 Winch handles with holder

DECK HARDWARE

• 8 Mooring cleats

• 1 Vertical electric windlass 1200 W with 3/8” gipsy

• Bow trampolines on each side of the composite central rostrum

• S/S stern pulpits with horseshoe buoy mount and flag holder

• S/S bow pulpits and forward lifelines

• S/S double lifelines

• S/S coach roof handrails

• Lifeline gates

COCKPIT

• Cockpit useable as outdoor salon, accessible via a stern walkway connecting both transoms

• Hard-Top Bimini with integral lighting

• Soft windshield for Bimini complete with full cockpit enclosure with clear panels

• Self-Bailing cockpit with teak grate

• Two person helm station on starboard roof bulkhead including: motor throttle controls, motor

control panels, steering compass, room for electronic instrument installation, leather covered

steering wheel with brake, double helm seat with cushions, access steps from cockpit with s/s

handrail, 2 line storage compartments

• Steering system: cable steering, composite shaft rudders, emergency tiller

• U-shape seating area with seat cushions covering generator & technical compartment

• Varnished wooden cockpit table interchangeable with salon coffee table

• 1 Aft cockpit seat locker

• 1 Port cockpit propane locker

• 2 Large storages area under steering station

• 2 Cockpit storage shelves

FOREDECK

• Forward seating area

• Covered chain locker

• Port & starboard storage lockers

• 1 Large central storage locker

• 1 Additional large locker on port side (owner’s version only)

• Forward bow lockers with locking deck hatches and access ladders

• Anchor roller on central composite rostrum with remote control electric windlass

TRANSOMS

• Starboard side hot and cold deck shower

• Starboard side s/s swim ladder

• Rubber transom rubrails

• Access to engine room

• Hot & Cold Transom showers on both port and starbord

ENGINE COMPARTMENT

• Access from opening hatch in transom

• 2 x 40 hp sail drive diesel installed by factory 12/’10 – 2011 models

• Motor shut off at helm station

• Double motor throttle control at helm station

• Motor compartment sound insulation

• Motor compartment air intake on aft crossbeam

• 12V Air exhaust fans

• 1 engine start battery 12V – 110 Ah

GENERATOR COMPARTMENT

• Sound insulated locker located under forward cockpit seat

• 1x21.5KWA (110V/ 60Hz/1800 rpm) diesel generator

• Automatic start and shut off depending on motor battery levels

• Generator start override switch on electrical panel

• Fuel filter with water separator

• Raw water filter

• Muffler with water separator

PLUMBING

• 3 X 175 L/2 = 46 gal water tanks = 138 gallons

• Fresh water circuit and 12V pump

• Hot water circuit with 40 L -11 gal water heater (includes heat exchanger to engines)

• Diesel capacity: 2 X 300 L/1 x 79 gal fuel tanks = 158 gals under starboard and port aft berth

• 2 x 12V automatic bilge pumps

• 2 x 12V manually activated bilge pumps

• 2 x Manual bilge pumps

• Fuel filter with water separator

• Raw water filter

• Exhaust with muffler

ELECTRICITY

• Backlit 12 V Electrical panel

• LCD display with: voltmeter, Ah-meter, water level gauge, diesel level gauge, low level alarm for diesel

and water tanks

• 2 Start batteries: 12V - 110 Ah

• 4 House batteries: 12V - 140 Ah

INTERIOR LAYOUT

• Interior woodwork in marine plywood and light oak alpi with horizontal grain

• Synthetic wenge, non-skid for the wood floor

OWNER’S VERSION

3 cabins, 3 heads, 3 separate showers

SALON

• Large panoramic view salon with glass sliding door and lock

• Standing headroom: 2.05m/6’9”

• 12V halogen salon overhead lights

• Seating for 8 people

• Varnished wood coffee table that can be swapped with smaller wooden cockpit table with1 set

of  tall aluminum legs and 1 set of shorter aluminum legs, both having protective cover

• Storage under settee

• 2 opening hatches in forward vertical roof windows

Chart table (on the port side on the salon, facing forward)

• Standing headroom: 1.95m/6’5”

• 12V halogen overhead light

• Panel for (optional) electronic equipment installation

• Swiveling stool that can be used as additional seat at the dining table

• Opening chart table

• Chart 12V reading light

Galley in Salon communicating directly with cockpit via a sliding glass bay window

• Standing headroom: 2 m/6’7”

• 12V halogen overhead lights

• White laminate countertop with wooden fiddles

• 3 burner stove

• Separate oven with grill

• 2 drawers

• Cupboard under sink with trash can behind door

• Storage under central seating area

• Overhead cupboards

• Additional storage areas designed for (optional) additional fridge or freezer, a dishwasher and

microwave oven

• 1 x12V fridge 130 L/34 gal (NEW – 2011)

Companionways

• Synthetic wenge non-skid steps

FORWARD STARBOARD CABIN

• Access through starboard passageway door

• Standing headroom: 1.95m/6’5”

• 12V Halogen overhead lighting

• 2 X 12V headboard reading lights

• “Semi - island style” berths with front and side access 2.0 m X 1.5 m/6’7” x 5’

• 1 drawer and 2 storage lockers on front of bed

• Lockers on both sides of bed

• 1 Hanging locker

• 1 Opening deck hatch with curtain

• 1 Hull port with curtain

• 1 Large one-way window with curtain

Forward starboard head

• Access from cabin

• 12 v halogen lighting

• Standing headroom: 1.95m/6’5”

• Large manual marine head with holding tank with gravity drain/ deck pump out (same holding

tank for front and aft WC)

• Fiberglass washbasin with hot/cold mixer tap, cupboards, mirrors

• 1 Opening deck hatch with blind

Forward starboard independent shower zone

• Access to shower stall through cabin

• Shower sump

• Roomy separate shower stall with hot/cold water mixer tap

• 1 Opening deck hatch with blind

• Standing headroom: 1.95m/6’5”

AFT STARBOARD CABIN

• Access through starboard passageway door

• Standing headroom: 1.85m/6’1”

• 12V Halogen overhead lighting

•  2 headboard reading lights

• “Semi - island style” berth with front and side access 2.0m X 1.5 m/6’7” X 5 ft

• 1 Drawer and 2 lockers on front of bed

• Lockers on both sides of berth

• 1 Hanging locker

• Access to emergency escape hatch

• Motor access under berth

• 1 Opening deck hatch with blind

• 1 Hull port with curtain

• 1 Large one-way window with curtain

Aft starboard head

• Access from aft starboard cabin

• 12 v halogen overhead lighting

• Standing headroom: ± 1.95 m or 6’5”

• Large manual marine head with holding tank with gravity drain/ deck pump out (same holding

tank for front and aft WC)

• Fiberglass washbasin with hot/cold mixer tap, lockers, mirrors

• 1 Opening deck hatch

Separate aft starboard shower

• Shower stall in same area as head but separated by a plexiglass door

• Standing headroom: 1.95 m/6’5”

• 1 Opening deck hatch with blind

OWNER’S HULL - Port owner’s hull includes:

•  Access from salon through sliding door in passageway

• 12 v halogen overhead lighting

•  2 Headboard reading lights

• “Semi - island style” berth with front and lateral access 2.0m X 1.5 m/6’7” X 5 ft

• 1 Drawer and 2 lockers on front of bed

• 1 Cabinet with 2 drawers on inboard side

• Lockers on both sides of bed

• 2 Large hanging locker

• Access to emergency escape hatch

• Motor access under bed

• 4 Opening deck hatches with blinds

• 1 Hull port with curtain

• 1 Large one-way window with curtain

• Sofa with 1 Vanity with shelves on the outboard side

Owners washroom

• Access from owner’s cabin

• 12 v halogen overhead lighting

• Standing headroom: ± 1.95 m/6’5”

• Large manual marine head

• Fiberglass washbasin with hot/cold mixer tap, lockers, mirrors

• 1 Opening deck hatch with blind

• 1 Opening hull port

• 1 Large one-way window with curtain

Owners forward port shower

• Shower stall in same area as head but separated by a plexiglass door

• Deck hatch with blind

Mattress and upholstery

• Cabins mattresses: marine mattress made of multi layer alveolar foam with several densities.

Mattress to improve comfort and safety for proper body regeneration (thickness: 20mm/5’)

Mattress treated: anti microbial, anti bacterial, non allergenic, anti dust mite

• Standard upholstery, synthetic fabrics adapted to marine environment:

-fabrics are sun resistant

-fabrics are water repellent, which includes anti stain treatment

• Fabric-covered wooden ceiling panels or fiberglass countermold in cabins and wash rooms

• Fabric hull liner in cabins

• Countertop molding in main salon

• Curtains in cabins and on forward windows in salon